## Slide 1: CSCI E-25 Computer Vision
Steve Elston
Copyright 2022, 2023, 2024, 2025, 2026, Stephen F Elston. All rights reserved.
Convolution and Image Filtering

## Slide 2: Image Filtering
Almost all computer vision pipelines require filtering
Without good image data preparation, state-of-the-art CV algorithms will not produce good results
Classical CV filters apply the mathematical operation of convolution
  Noise suppression
  Edge and corner enhancement
  Anti-aliasing
  Resampling
We can understand the effects of filtering through spectral analysis
  Filter changes power spectrum of image
  Typical filters reduce high-frequency energy – noise
  Higher frequency components include sharp edges and corners – typically blurred by filtering

## Slide 3: Image Filtering
Common digital image problems
Poor lighting conditions
Low or limited contrast camera sensors
Limits of image sensor resolution
Noisy image sensors
Environmental conditions, fog, smoke, etc.
Occlusion of objects of interest
Poor geometry of camera placement
…

## Slide 4: Image Filtering
Key points for this lesson
Convolution in 1-d, and 2-d
Applying padding, stride and tiling for convolution
Constructing convolutional filter kernels
Linear separation of convolutional kernels
The Fourier transform and frequency components of images
The relationship between filtering and the spectrum of images
Importance of scale and application of multiscale image pyramids

## Slide 5
Convolution

## Slide 6: Convolution
Convolution operations are a computationally efficient method of applying filters
Convolutional kernel weights determine characteristics of filters
  Filtering noise
  Creating and enhancing features
Convolutional filtering is computationally efficient
  High volume applications
  Real-time CV

## Slide 7: Convolution
Convolution operations are a computationally efficient method of applying filters
Discrete convolutional kernels have a span, measured in points or samples
Kernel moves over image, a stride length at a time, producing filtered output
Typically stride span
Tiled filters do not overlap, stride = span

## Slide 8: Convolution
Convolution operations are a computationally efficient method of applying filters to discretely
Convolution kernel is moved along the input tensor
  Kernel has a small span compared to dimension of input tensor
  At each step a weighted output value is computed
  Output tensor can have different number of dimensions from input tensor
1-D convolutions are a simple, but useful example
  Time series data
  Speech
  Medical signals

## Slide 9: 1-D Convolution
1-D CNNs are a simple, but useful example
Consider a convolutional kernel with a span of 3 and stride 1
Kernel defined by weights
The convolved value is the weighted sum over the span of the convolutional kernel
W1
W2
W3
t = 3
Kernel Span
or
Receptive Field

## Slide 10: 1-D Convolution
1-D CNNs are a simple, but useful example
Move kernel by stride 1
The convolutional kernel moves one sample per step
t = 4
Kernel Span
or
Receptive Field
W1
W2
W3

## Slide 11: 1-D Convolution
1-D CNNs are a simple, but useful example
Continue to produce one output value per time step
t = 5
Kernel Span
or
Receptive Field
W3
W1
W2

## Slide 12: 1-D Convolution
1-D CNNs are a simple, but useful example
Convolution ends when end of series reached
For odd span, output is )/2, shorter than original series
t = n
Kernel Span
or
Receptive Field
W1
W2
W3

## Slide 13: 1-D Convolution
Mathematically, express 1-d convolution as a weighted sum over a set of discrete kernel values:
Where:
the output of the convolution operation at time t
series of values
k convolution kernel weight vector of length
convolution operator
time difference of the convolution operator
, for odd length operator

## Slide 14: 2-D Convolution
Input
Output
4 x 4 input tensor
3 x 3 convolution operator, stride = 1
2 x 2 output tensor

## Slide 15: 2-D Convolution
We can extend convolution in higher dimensions
Mathematically, we express 2-d convolution as a weighted sum over a discrete rectangular kernel
For square kernel, , of odd dimensions , convolution can be expressed
  Where
  kernel span
  2-d convolution results
  2-d input image
  2d convolutional kernal weight tensor of dimension

## Slide 16: 2-D Convolution
How can we extend convolution to higher dimensions
The image and kernel tensors are commutative in the convolution relationship
This allows an operation known as kernel flipping with the following alternative result expressed

## Slide 17: Algebraic Properties of Convolution
Convolution operations have useful algebraic properties
Notice five of these properties are identical to the familiar algebraic properties of multiplication
Name | Property
Commutativity | 
Associativity | 
Distributivity | 
Associativity of scalar multiplication | 
Translation (shift) invariance | 
Name | Property
Commutativity | 
Associativity | 
Distributivity | 
Associativity of scalar multiplication | 
Translation (shift) invariance | 

## Slide 18
Stride, Tiling and Padding for Convolution

## Slide 19: Stride and Tiling
Do we always move the convolution kernel by stride 1 (1 sample)?
No!
  May not need the full resolution of the input
  Or, change the dimension of the input tensor
Stride > 1 down-samples the data
  Output of lower resolution
Stride < 1 up-samples the data
  Use fractional stride
  Output of higher pixel count
  Or, use transposed convolution – more on this later
Use fractional stride to compute tensor with required output dimension

## Slide 20: Stride and Tiling
Input
Output
Stride
Stride
Tiling is a special case when stride = span
Stride >1 reduces dimensionality, down-sampling

## Slide 21: Padding for Convolution
How can we deal with edges of the input tensor when performing convolution?
We always work with a finite spatial and temporal (video) sample creating edge effects
A valid convolution confines the kernel to the input tensor dimensions
  For odd kernel shape, output dimension is (span + 1)/2 less than input dimension
  After many convolution layers, dimension is reduced further
We can zero pad the input tensor
  Dimensionality is maintained
Use circular convolution
  Wrap the ends of the finite sample to form a ‘circle’ creating a continuous sample
  Can wrap in multiple dimensions

## Slide 22: Padding for Convolution
Input
Output
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Convolution
Operations
Dimension of output tensor = dimension of input tensor
0 values have little effect with max pooling
Example: 4x4 input tensor with 3x3 kernel

## Slide 23: Circular Convolution
Input
Output
v
v
0
v
v
Convolution
Operations
Dimension of output tensor = dimension of input tensor
Example: 4x4 input tensor with 3x3 kernel
Values are wrapped from the other side of the sample

## Slide 24
Commonly Used Convolution Kernels

## Slide 25: Common Convolution Kernels
Convolutional filters are widely used for image enhancement in CV pipelines
Image processing packages support many convolutional filters
  The Scikit-Image Filters package has a wide selection of filters
  The OpenCV Image Processing Models supports many more filter types
We will only review a few convolutional filters here
We will investigate convolutional neural networks in subsequent lessons

## Slide 26: Common Convolution Kernels
A moving average kernel has equal weights
Example, a 3 x 3 moving average kernel
This is also known as a blur filter or box blur
Notice the normalization so weights add to 1.0

## Slide 27: Common Convolution Kernels
A Gaussian kernel smooths an image
Weights computed from Gaussian function with span parameter :
Example, a 3 x 3 Gaussian kernel,
Then Gaussian kernel limits the bandwidth and blurs the image
Larger narrower bandwidth of the Gaussian kernel

## Slide 28: Common Convolution Kernels
A Gaussian kernel smooths an image
Weights computed from Gaussian function with span parameter :
We create approximate Gaussian kernels with the binomial approximation
Credit, Antonio Torralba, Lecture 2016

## Slide 29: Common Convolution Kernels
A Gaussian kernel smooths an image
Weights computed from Gaussian function with span parameter :
The binomial approximation is separable
  Compute by independent convolutions along each axis
  Computationally efficient approach
Constructing the 2-d Gaussian kernel, from 1d binomial filters

## Slide 30: Common Convolution Kernels
Example of Gaussian kernel filtering of image
Broad band Gaussian Filter
Narrow band Gaussian Filter

## Slide 31: Common Convolution Kernels
The Sobel kernel takes the first derivative of the image
Compute the gradients (partial derivatives) of the image, , along each axis
Here,, is the convolution operator
Notice the sum of the weights is 0
Other derivative kernels can be derived, e.g.

## Slide 32: Common Convolution Kernels
The Sobel kernel is an example of a separable kernel
Notice that we can write a Sobel kernel as the product of two 1-dimensional kernels
For computational efficiency a 2-dimensional separable kernel can be applied as 2 convolution of 1-dimensional kernels

## Slide 33: Median Filter
Median filter is a special case
Median filter outputs median value of the pixel values within patch
  Typically use odd patch sizes – e.g., 3 x 3, 5 x 5, 7 x 7
Median filter is not easily formulated using convolution
  Use an incremental update algorithm for computational efficiency
Median filter has interesting properties
  Suppresses noise
  Sharpens edges and corners
Median filter can alter image
  Response is not isotropic – not same along diagonals of image
  Can move edges and corners

## Slide 34
Filtering and Spectral Properties of Images

## Slide 35: Spectral Properties of Images
The power spectrum of an image reveals fundamental properties
Power spectrum reveals the vertical and horizontal frequency components of the image
Low frequency components of an image represent regions with slowly changing properties
High frequency components of an image arise from local features with rapid changes
  Edges
  Corners
  Texture
Filtering changes the power spectrum of an image

## Slide 36: Spectral Properties of Images
We can decompose an image into frequency components using a Fourier transform
The Fourier transform decomposes a signal into frequency components
  Is a linear transform from time domain to frequency domain
The 1-dimensional Fourier transform of a function, , in the space or time domain can be expressed:
is the complex spectrum of , in the frequency domain
  Imaginary component is phase at frequency
  Magnitude of the complex number is amplitude at frequency

## Slide 37: Spectral Properties of Images
We can decompose an image into frequency components using a Fourier transform
The Fourier transform decomposes a signal into frequency components
is the complex spectrum of
  Imaginary component is phase, , at frequency
  Magnitude of the complex number is the signal amplitude at frequency
Amplitude
Credit, Wikipedia commons
Two sinusoidal signals with identical frequency and amplitude, phase shifted by q

## Slide 38: Spectral Properties of Images
We can decompose an image into frequency components using a Fourier transform
The Fourier transform decomposes a signal into frequency components
Apply Euler’s formula,
  And,
Signal at frequency is the linear superposition of cosine and complex (phase) sine components
Credit, Wikipedia commons
Two sinusoidal signals with identical frequency and amplitude, phase shifted by q
Amplitude

## Slide 39: Spectral Properties of Images
We can decompose an image into frequency components using a Fourier transform
The Fourier transform decomposes a signal into frequency components
For our purposes, we mostly care about the power spectrum
Power spectrum depends on magnitude only, not phase
Amplitude
Credit, Wikipedia commons
Two sinusoidal signals with identical frequency and amplitude, phase shifted by q

## Slide 40: Spectral Properties of Images
Example of single frequency signals and their power spectrum
Phase shifted signal
Power spectrum invariant to phase

## Slide 41: Spectral Properties of Images
Example of signal with two frequencies and the power spectrum

## Slide 42: Spectral Properties of Images
Impulse response of a convolutional filter is the Fourier transform in the frequency domain
Response in time (or frequency) domain
Response in frequency (or time) domain
Relationship is invertible (inverse Fourier transform) and commutable: exchange time and frequency
Credit, DSP Illustrations
Fourier Transform

## Slide 43: Spectral Properties of Images
Impulse response of some commonly used convolutional filters, showing:
Name of the filter
Values of the kernel operator
Analytic representation of the Fourier transform
Graph of the Fourier transform or impulse response
Credit: Szeliski, 2nd Edition, 2022

## Slide 44: Spectral Properties of Images
For discretely sampled images we use a 2-dimensional discrete Fourier transform
The discrete Fourier transform is sampled over image samples (pixels), , and discrete frequencies, , within the Nyquist limit:
( )
  is the spatial index of a discrete pixel
  are discrete horizontal and vertical frequencies
This looks like a convolution!
  2d Kernel

## Slide 45: Spectral Properties of Images
For discretely sampled images we use a 2-dimensional discrete Fourier transform
The discrete Fourier transform is sampled over image samples (pixels), , and discrete frequencies, , within the Nyquist limit:
( )
  is the spatial index of a discrete pixel
  are discrete horizontal and vertical frequencies
Notice the limited spatial range of the sampling
  Not
  Limited spatial sampling introduces edge artifacts – edges of images are impulses

## Slide 46: Spectral Properties of Images
For a discretely sampled image we use a 2-dimensional discrete Fourier transform
The discrete Fourier transform is sampled over image samples (pixels), , and discrete frequencies, , within the Nyquist limit:
( )
Appling Euler’s formula, , we get:
( )
This form makes the real (cos) and imaginary or phase (sin) components explicit

## Slide 47: Spectral Properties of Images
The power spectrum of an image reveals fundamental properties
Spectral density reveals the power or energy in vertical and horizontal frequency components of the image
In words, the spectral density is the square of the absolute value of the magnitude of the estimated Fourier transform
The spectral density function is computed over all frequency components up to the Nyquist limit

## Slide 48: Spectral Properties of Images
The power spectrum of an image reveals fundamental properties
Spectral density reveals the power or energy in vertical and horizontal frequency components of the image given the estimated Fourier transform,
Spectral density is easier to work with, since it gives us the real-valued power at each frequency,
  The squared magnitude of the signal at
Notice that, unlike Fourier transform, the spectral density is not invertible
  The square of absolute magnitude of loses phase information

## Slide 49: Spectral Properties of Images
For real-valued image, spectral density is symmetric about zero frequency
Rapid changes (e.g. edges, corners) are the high frequency components
Vertical frequency = 0
Spectral density reveals the power or energy of vertical and horizontal frequency components of the image
Horizontal frequency = 0
Increasing vertical frequency
Increasing vertical frequency
Increasing Horizontal frequency
Increasing Horizontal frequency

## Slide 50: Spectral Properties of Images
Example; image with vertical and horizontal composite sinusoidal components
Power spectrum of image shows peaks at horizontal and vertical frequency components – notice the symmertry
Spectral density reveals the power or energy in vertical and horizontal frequency components of the image

## Slide 51: Spectral Properties of Images
Example; image with vertical and horizontal composite sinusoidal components
Notice that rotating the sinusoidal pattern by reverses the sign of the spectral componentsm, but maintains symmetry
Spectral density reveals the power or energy in vertical and horizontal frequency components of the image

## Slide 52: Spectral Properties of Images
Filters change the spectral characteristics of images
Equalization distributes the power spectrum more uniformly
Equalization boosts higher frequency components
Changes in spectral density show the effect of filtering
Contrast Limited Adaptive Histogram Equalization

## Slide 53: Spectral Properties of Images
Filters change the spectral characteristics of images
Filters can suppress unwanted high frequency noise
Filtering reduces aliasing
Lower frequency image is blurred – edges and corners less sharp
Changes in spectral density show the effect of filtering
Gaussian Filter
s = 1.0

## Slide 54: The Convolution Theorem
There is a direct relationship between filtering in the spatial (or time) domain and the frequency domain, by the convolution theorem
For spatial domain image, , and its Fourier transform, , operating on by a spatial domain convolutional kernel, , and ts Fourier transform, , we can state the convolution theorem:
In words, the convolution theorem states that convolution in the spatial domain is equivalent to the inverse Fourier transform of the point wise product of the Fourier transforms of the image and the kernel, and vice versa
The convolution theorem helps us understand the effects of filtering

## Slide 55
Gaussian Filtering and Image Pyramids

## Slide 56: Image Pyramid Example
Search an image for objects matching a template
Similar objects in the image can appear with different scales
Template has fixed scale
Image credit, Lecture slides, Sitzmann, Konaković Luković, and Freeman, 2023
Template

## Slide 57: Image Pyramid Example
Search an image for objects matching a template
Using only 1 scale leads to poor results
Template
Search with template
Result
Image credit, Lecture slides, Sitzmann, Konaković Luković, and Freeman, 2023

## Slide 58: Image Pyramid Example
Search an image for objects matching a template
Search on multi-scale pyramid leads to scale intendent results
More satisfactory result
Template
Image credit, Lecture slides, Sitzmann, Konaković Luković, and Freeman, 2023

## Slide 59: Gaussian filtering and down sampling
Use Gaussian filtering allows down sampling without aliasing
Convolve image with Gaussian filter
Subsampling performed at stride >1
Filtering image to lower resolution eliminates aliasing
Create image pyramid by Gaussian down sampling by octaves (factor of 2)

## Slide 60: Summary
Key points for this lesson
How convolutional works in 1-d, 2-d and higher dimension
How to apply padding, stride and tiling for convolution
Constructing convolutional filter kernels
Linear separation of convolutional kernels
The relationship between filtering and the spectrum of images
Image pyramids address the issue of multiple scales in images