## Slide 1: CSCI E-25 Computer Vision
Steve Elston
Copyright 2021, 2022, 2023, 2024, 2025, Stephen F Elston. All rights reserved.
Feature Extraction

## Slide 2: Feature Extraction
Computer vision algorithms require features
Feature extraction is a foundation many CV algorithms
Classical CV relies on extraction of hand-engineered features
  Long history starting in 1970s
  Often computationally efficient for high-volume and real-time
  Still used in CV pipelines
Deep neural networks learn a feature set
  Have superseded classical methods in many cases
  But often computationally intensive
  Much more on this later!
In many cases, preprocessing with classical methods can improve DL algorithm performance!

## Slide 3: Feature Extraction
Many applications and types of feature extraction algorithms
Commonly used features
  Edges
  Corners and other interest points
  Textures
A few widely applied applications
  Locating and identifying objects in images
  Stitching images together
  Models of motion from a series of images – optical flow
  Stereo vison and constructing 3-dimensional scenes
  Efficient image and video search

## Slide 4: Feature Extraction
Example: How has the image transformed between the images?
Locate interest points or key points
For patches around the interest points extract statistics - descriptors
Matching points are identified by descriptors
Images can be warped to match – a machine learning problem
B1
B2
B3
A1
A2
A3

## Slide 5: Feature Extraction
Key points for this lesson
Use of gradients to detect edges
Decomposition of gradients as general interest point detectors
How Harris corner detector works
Using statistics of gradients to construct descriptors - HOG
How to identify interest points with the SIFT algorithm
The basics of the BRIEF algorithm
Interest point detection across scales

## Slide 6
Finding Edges and Gradients

## Slide 7: Finding Edges
Edges are identified by rapid changes in image properties
Edges have high perpendicular gradients
  Edges can have any orientation
  Detector must be rotationally invariant
Could use magnitude of gradient
  But gradient is an unstable and requires thresholding
  Sobel and Canny filters are examples
Use second derivative or Laplacian
  The zero-crossing of the Laplacian is the location of the edge
  The Laplacian of the image intensity :
  +

## Slide 8: Finding Edges with Sobel Filter
Sobel filter is an early attempt at using an approximately isotropic gradient estimate
Uses a pair of operators to compute gradient components of image array,
Magnitude of the gradient is then

## Slide 9: Finding Edges with Sobel Filter
Sobel filter is an early attempt at using an approximately isotropic gradient estimate
For computational efficiency we can reformulate the

## Slide 10: Finding Edges with Sobel Filter
Sobel filter is an early attempt at using an approximately isotropic gradient estimate
Magnitude of the gradient is
Must threshold the gradient, , to filter edges
There are other similar operators that can produce better approximations of the gradient magnitude

## Slide 11
Finding Edges with Gradients with the Canny Filter

## Slide 12: Finding Edges with Canny Filter
Canny filter is a sophisticated multi-stage algorithm for finding edges in images
Detects edges with a low error rate
Accurately locates the edge
Each edge in the image should only be marked once

## Slide 13: Finding Edges with Canny Filter
Canny filter is a sophisticated multi-stage algorithm for finding edges in images
We will not explore the details here
Basic steps of the algorithm:
  Apply a Gaussian filter to smooth edges and remove noise
  Compute the intensity (magnitude) of the gradients, e.g. with Sobel filter
  The gradients are filtered using a double threshold with upper and lower bounds on the gradient to identify potential edge pixels
  Filter pixels of appropriate magnitude (by threshold) with a hysteresis algorithm to find adjoining pixels likely to be part of edges

## Slide 14
Finding Edges With Laplacian

## Slide 15: Finding Edges
Edges are identified with the Laplacian operator
+
Applying a Laplacian kernel to an edge gives a distinctive signal:
Edge is at the zero crossing of the convolved image
Convolution with Laplacian
Credit, R. Fisher, S. Perkins, A. Walker and E. Wolfart

## Slide 16: Finding Edges
Edges are identified by convolution with the Laplacian operator
+
Simple Laplacian kernel:
Laplacian kernel with less directional bias:

## Slide 17: Finding Edges
Laplacian of a Gaussian reduces noise
The Laplacian operator is effective at finding edges, but susceptible to noise
Credit, R. Fisher, S. Perkins, A. Walker and E. Wolfart
Reduce noise by using Laplacian of a Gaussian filter kernel or Laplacian of Gaussian ():
Notice, the is symmetric and therefore rotationally invariant

## Slide 18: Finding Edges
Difference of Gaussian filtered images
How close is the difference of Gaussian filtered image to the full formulation?
The approximation is generally quite close
Gray-scale then difference of Gaussians
Credit, Wikipedia commons

## Slide 19
Edges and the Hough Transform

## Slide 20: Why Enhance Edges?
Edge detection algorithms only operate locally
Only pieces of edges may be detected
  Parts of an edge may be occulated by other objects in the image
  Gradients along edges may vary considerably
We can use a Hough transform to enhance edges in an image
Many versions of Hough transform have been developed
In order of computational complexity and practicality
  Straight line: our focus here
  Circles and ellipses
  Arbitrary curves and shapes
  3D surfaces

## Slide 21: Straight Line Hough Transform
Straight line Hough transform uses a simple voting algorithm to find lines in images
Straight lines are common in human environments
How to parameterizing a line?
Why not use ?
m becomes extreme as line becomes steeper
For a vertical line !
x
y

## Slide 22: Straight Line Hough Transform
Straight line Hough transform uses a simple voting algorithm to find lines in images
How to parameterizing a line?
Use the Hesse normal form
Hesse normal form parametrizes in terms of a perpendicular between the line and the origin
Perpendicular has angle with respect to the x axis and length r
Hesse normal form works for lines in any orientation!
x
y
r

## Slide 23: Straight Line Hough Transform
Straight line Hough transform uses a simple voting algorithm to find lines in images
Hough transform uses a parameter search for edges
Search grid is constrained, typically
For an edge at each value of and there are an infinite number of possible lines
x
y

## Slide 24: Straight Line Hough Transform
Straight line Hough transform uses a simple voting algorithm to find lines in images
A line is intersected at many points in , , space
These intersections sweep out sinusoidal curves in , , space
These intersections are accumulated in an array representing the , , space
Peaks in the accumulator space represent the , parameters of detected lines
x
y

## Slide 25: Straight Line Hough Transform
Hough transform example
Start with a synthetic image
Contains 3 lines

## Slide 26: Straight Line Hough Transform
Hough transform example
Hough transform accumulator has three peaks, corresponding to 3 detected lines

## Slide 27
Interest Point Detection

## Slide 28: Interest Point Detection
Interest points are important features for many CV algorithms
Edges are problematic
  Too dense – creates alignment ambiguity between views
  No unique characteristic – lines are similar
  Poor localization – features are elongated
Interest points are better
  Tend to be sparse
  Often have unique identifiable characteristics
  Points – high location specificity
Other terms for interest points
  Key points
  Feature points

## Slide 29: Interest Point Detection
Interest point detection
Why can’t we just use gradients?
Consider the example of a diagonal edge
Diagonal edge has strong perpendicular gradient
Gradient in x and y is same along line segment – poor localization

## Slide 30: Interest Point Detection
Corners detection is more complex than edge detection
Edges, and curves, have a well defined perpendicular
  Locally only one degree of freedom, orientation
Corners have two degrees of freedom
  Orientation
  Angle between the edges forming the corner
Examples

## Slide 31: Interest Point Detection
Corners are a special case of the more general concept of interest points
Interest points occur where ever lines intersect
Examples:
  Crossing intersection
  Oblique crossing intersection
  T intersection
  Complex intersection

## Slide 32: Interest Point Detection
Interest points have more complex gradients than edges
Use convolutional kernel to estimate gradients
Areas of similar intensity
  No localization, leads to problems!
Edges have simple perpendicular gradients
  Poor localization
Other interest points have rapidly changing gradients in several directions
Similar intensity: Small gradient in all directions
Edge: Large perpendicular gradients
Interest point: Large gradient in all directions

## Slide 33: Interest Point Detection
Interest point detection approach
Recall that we locate edges with gradient-based algorithms
Interest points can be identified by localized intensity changes
Consider the second order Taylor series expansion of local intensity for a point in 2-dimensional space about an origin, :
Using the streamlined notation, , the symmetric matrix of second derivatives is:

## Slide 34: Interest Point Detection
Interest point detection approach
To understand these algorithms, we need to dig into some details of gradients
Given a window function, , we can write the energy functional, , for a shift :
Weighted sum of squared differences in intensity is the energy function
Expand the energy function in quadratic form using matrix notation:

## Slide 35: Interest Point Detection
Interest point detection approach
Expand the energy function in quadratic form using matrix notation:
Zero gradient at origin ,
Quadratic form of

## Slide 36: Interest Point Detection
Interest point detection approach
Simplify the quadratic form:
  The energy is 0 at the origin:
  The gradient is 0 at the origin:
The quadratic energy function is then:

## Slide 37: Interest Point Detection
Interest point detection approach
How to interpret the local properties of the Hessian matrix, :
By applying a rotation, , we can diagonalize the matrix
are the eigenvalues

## Slide 38: Interest Point Detection
Interest point detection approach
By applying a rotation, , we can diagonalize the Hessian matrix with eigenvalues :
direction of the slowest change
direction of the fastest change
(max)-1/2
(min)-1/2
Eigenvalues characterize the curvature
Eigenvalues parameterize curvature in the maximum and minimum directions

## Slide 39: Interest Point Detection
Interest point detection approach
Eigenvalues of the Hessian, , characterize the curvature
Values of are indicators of:
  Flat region: , and small
  Edge: or , and large
  Corner or other interest point: , and large
1
2
“Corner” 1 and 2 are large, 1 ~ 2; E increases in all directions
1 and 2 are small; E is almost constant in all directions
“Edge” 1 >> 2
“Edge” 2 >> 1
“Flat” region

## Slide 40: Interest Point Detection
Interest point detection approach
How do we create an interest point detector from the Hessian?
Can we just use a threshold on the are the eigenvalues, ?
In many cases, no! Too much noise
Consequently, a great many interest point detectors have been developed
The Harris detector (1985) is one of the oldest; is robust and still used

## Slide 41
Harris Algorithm

## Slide 42: Harris Interest Point Detection
Harris interest point detection algorithm
For efficiency, the Harris interest point detector avoids directly computing the eigenvalues
Two properties of symmetric matrices:
The threshold, , is then applied to the following quantity to find interest points
Typical values
Apply non-maximal suppression

## Slide 43: Harris Interest Point Detection
Harris interest point detection algorithm
Adjust, filter and convert image to gray-scale
Using a Gaussian weighted window, , compute the matrix for each (overlapping) patch of the image
Apply the threshold function of each patch – non-maximal suppression by selecting the points with largest value of in local regions

## Slide 44: Harris Interest Point Detection
Steps of Harris interest point detection algorithm
Adjust, filter and convert image to gray-scale
Image from slide by S. Lazebnik

## Slide 45: Harris Interest Point Detection
Steps of Harris interest point detection algorithm
Using a Gaussian weighted window, , compute the matrix for each (overlapping) patch of the image – It’s convolution!
Image from slide by S. Lazebnik

## Slide 46: Harris Interest Point Detection
Steps of Harris interest point detection algorithm
Apply the threshold function of each patch
Image from slide by S. Lazebnik

## Slide 47: Harris Interest Point Detection
Steps of Harris interest point detection algorithm
Perform non-maximal suppression, by selecting the points with largest value of in local regions
Image from slide by S. Lazebnik

## Slide 48: Harris Interest Point Detection
Why is the Harris algorithm shift and rotationally invariant
Shift invariant: The convolutional Laplacian gradient kernel is applied across the image
  Response of convolution only depend on local gradient, not location
Rotationally invariant: The eigenvalues are rotationally invariant
  Eigenvectors project the gradient values to the principal axes
  Eigenvalues remain unchanged
Not scale invariant: The response of the Laplacian operator changes with local gradient and scale of the operator, s

## Slide 49
Gradients and Features – the HOG Algorithm

## Slide 50: Gradients and Features
Gradients are powerful features
Patterns of direction of maximum gradient can help identify objects in the image
But gradients are extremely noisy
Idea; average histogram of gradients over patches on the image
Basis of the Histogram of Oriented Gradients (HOG) algorithm, Dalal and Triggs (2005)
HOGs generate powerful features
  Particularly good for objects with long linear features
Computationally intensive
Typically apply HOG to each color channel or convert to gray-scale

## Slide 51: Gradients and Features
Many variations and details for HOG algorithms
Prepare the image, required for consistent gradient estimation
  Resize
  Convert to grayscale
  Local equalization
Compute gradients around each pixel
Divide image into cells (often ), weight gradients and compute histograms with 8 orientations
  Log-polar coordinate weighting
Block normalize histograms (often blocks)
  Usually, L1 or L2 norm
Result is features per-block

## Slide 52: Gradients and Features
Basic steps of HOG algorithms
Gradients of image patch
Histogram in log-polar coordinates
Normalized feature vector
Adapted Stanford CS-131 slides Neibles and Wu

## Slide 53: Gradients and Features
Example of HOG – features to identify a bicycle
Adapted Stanford CS-131 slides Neibles and Wu

## Slide 54
Interest Point Descriptors

## Slide 55: Interest Point Descriptors
Must identify interest points between complex images
Matching interest points can be difficult
Image from Oxford Dataset, Mikolajczyk, et. al., 2005

## Slide 56: Interest Point Descriptors
Must identify interest points between complex images
Can we just use the set of interest points?
Not directly, can’t tell the features apart
Need to use properties of the regions - descriptors
Some ideas
  Intensity
  Color ratios
  texture
  Local gradient statistics ✔

## Slide 57: Interest Point Descriptors
Must identify interest points between complex images
Harris detector is not scale independent – not suitable
But, Harris detector identifies this feature as a series of edges
Harris detector identifies this feature as a corner

## Slide 58: Interest Point Descriptors
Must identify interest points between complex images
How well can intensity or color ratios identify features
Create intensity histograms for region (patch) around feature
Small shifts and rotations can change intensity and histogram
Need a more invariant solution!
Figure by Andrew Zisserman

## Slide 59: Interest Point Descriptors
Must uniquely identify interest points between complex images
Need a more invariant solution!
Scale invariant
Shift invariant
Rotationally invariant

## Slide 60: Interest Point Descriptors
Key properties of good descriptors
Locality: features describe parts and are robust to occlusion and clutter (no prior segmentation)
Distinctiveness: identifiable from a large database of objects
Quantity: many features distinctive can be generated even for small objects
Efficiency: close to real-time performance
Extensibility: can easily be extended to wide range of differing feature types, each adding robustness to changes

## Slide 61: Interest Point Descriptors
Must identify interest points between complex images
Many shift and rotationally invariant algorithms have been developed:
  SHIFT
  SURF
  DAISY
  BRIEF
  CENTURE
  …
Use hierarchy of scales with interest point descriptors

## Slide 62
SHIFT Algorithm

## Slide 63: The SIFT Algorithm
Scale Invariant Feature Transformation (SIFT)
SIFT developed by David Lowe (1999 and 2004)
Algorithm
  Divide image into patches
  Divide a array of pixels into 16 cells
  Compute the gradients at each pixel
  Create a 8-direction histogram of gradient direction for each cell, gives features
  Normalize the descriptor so that:

## Slide 64: The SIFT Algorithm
Scale Invariant Feature Transformation (SIFT)
Gradients computed for pixel array
8-direction histograms for each cell
Descriptor is normalized histogram values
Adapted from slide by David Lowe

## Slide 65: The SIFT Algorithm
How can SIFT be made rotationally invariant?
Start with the gradients on the grid
Find the mean gradient direction
Histogram directions are computed relative to the mean direction
General approach to rotational invariance used with other descriptors
Adapted from slide by David Lowe

## Slide 66
The BRIEF Algorithm

## Slide 67: The BRIEF Algorithm
The BRIEF feature descriptor is an efficient and robust feature descriptor
- Steps of the BRIEF algorithm:
For each interest point in each image define a sample patch
Random sample two pixels from the patch
Compute the binary statistic, in the set ,
Add the statistic to the mini-hash
Repeat steps 2-4 until bits of the mini-hash
For each possible pair of patches in two images compute the Hamming distance
Match interest points with highest similarity, small Hamming distance

## Slide 68: The BRIEF Algorithm
How is the binary mini-hash string computed?
BRIEF computes the binary values of the mini-hash by the following relationship:
The n binary values are organized into the dimensional binary mini-hash:
Differences between descriptors is the Hamming distance

## Slide 69: The BRIEF Algorithm
How are the pixels sampled?
Pairs of pixel locations, , in the patch are randomly sampled
The binary statistic, , is computed given the pixel values,
The binary value is added to the mini-hash vector
Calonder, et.al. found Gaussian sampling is generally best

## Slide 70: The BRIEF Algorithm
How can you find the Hamming distance?
For binary strings, Hamming distance is the XOR between the strings
XOR is often supported by CPU - very fast and massively scalable!
Example: Let and , the Hamming distance is:

## Slide 71: The BRIEF Algorithm
Example of difficult interest point problem
Wall image from Calonder, et.al.

## Slide 72: The BRIEF Algorithm
How well does the BRIEF Algorithm work?
Calonder, et.al. show that there is diminishing improvement beyond a 256 bit (256 test) mini-hash
Computation of only 256 binary statistics, , is fast per patch
The limit of correct recognition depends on the nature of the images
Wider angles between images reduce recognition with all descriptors

## Slide 73
Multi-Scale Interest Points

## Slide 74: Multi-Scale Feature Identification
Pyramid structure enables extraction of interest points at several scales
Pyramid scales from fine to coarse in octaves
Features at each scale extracted
Can use a variety of interest point descriptor algorithms
  SIFT
  Harris – Laplacian
x
Diagram by Saad Bedros

## Slide 75: Multi-Scale Feature Identification
Scaling using Laplacian or DoG
Scaling applies convolution with kernel, , on image :
Laplacian
DoG
Where Gaussian is:
Both kernels are rotationally invariant

## Slide 76: Multi-Scale Feature Identification
Scaling DoG
Scaling applies convolution with kernel, , on image :
Example: pyramid with DoG,
Diagram by Krystian Mikolajczyk

## Slide 77: Multi-Scale Feature Identification
Scaling DoG
Scaling applies convolution with kernel using
Determine scale with maximum of descriptor
Adapted from diagram by Krystian Mikolajczyk

## Slide 78: Summary
Key points for this lesson
Use of gradients to detect edges
How decomposition of gradients is used for general interest point detection
How Harris corner detector works
Using statistics of gradients are used to construct descriptors
How to identify interest points with the SIFT algorithm
The basics of the BRIEF algorithm
How to detect interest points across scales