## Slide 1: CSCI E-25 Computer Vision
Steve Elston
Copyright 2021, 2022, 2023, 2024 Stephen F Elston. All rights reserved.
Homography and Projections

## Slide 2: Homography and Projections
How do we transform between light scattered off objects and projections on a camera image plane?
Use planar projective transformation to model projection of an object to a camera image plane
Use projection to transform one camera pose to another
Inverse transform from image planes to real-world object location
Planar transformations use projection matrix

## Slide 3: Homography and Projections
Projections are used in many computer vision applications
Warping images to adjust for camera viewpoint, aka, camera pose
Tracking moving objects – a.k.a. optical flow
Stitching images together
3D computer vision
Integrating different imaging types, e.g. lidar and optical – beyond scope of our course
…

## Slide 4: Projective Geometry
Projective transform changes view on image plane
Projections of 4 points on a line
Transformation projects one view to another on the image plane
Planar transformation have common Optical center
w
Optical center
Projection 1
Image plane
Projection 2

## Slide 5: Projective Geometry
Location of points and lines in space is ambiguous in a single camera view
4 points along a line on different world planes
All 3 sets of points fall at the same points on the image plan
Planar transformation are ambigiuous
w
Image plane
World
Plane 1
Optical center
World
Plane 2
World
Plane 3

## Slide 6: Stereo Vision Problem
Stereo vision is a canonical problem in computer vision
Can locate a point in 3-D space from location on 2 or more image planes
Requires a model for the cameras
  Intrinsic properties of cameras
  Scene extrinsic from cameras
Solve system of camera equations to locate point in 3-D space
w
x1
x2
Image plane 2
Image plane 1
Optical center 2
Optical center 1

## Slide 7: Image alignment
Example: How to align images from two views?
Locate interest points
For patches around the interest points extract statistics - descriptors
Matching points are identified by descriptors
Images can be warped to match – use image transformations
B1
B2
B3
A1
A2
A3

## Slide 8: Pinhole Camera Model

## Slide 9: Pinhole Camera
Pinhole camera is a canonical model for image formation
First known description by Chinese philosopher Mo Ti (Mozi) in 5th Century BCA
Described by Greek philosopher Aristotle in 4th century BCA
Known in Europe as Camera Obscura from about the 10th Century
Pinhole camera is a chamber with a small hole on one side

## Slide 10: The Nature of Images
Basic image camera image formation
A camera forms an image from scattered light from an object
A pinhole camera or camera obscura forms an image by projecting light rays back to their source
Credit, Wikipedia commons

## Slide 11: Pinhole Camera
Pinhole camera is a canonical model for image formation
Pinhole camera is a chamber with a small hole on one side
Image on side of chamber opposite hole
Use cartesian coordinates on the image plane
Pinhole is the origin of the coordinate system
Transform from real-world coordinates to image plane coordinates

## Slide 12: The Nature of Images
Basic image camera image formation
The smaller the aperture of the pinhole the light is focused to a point and the image is sharper, but less light passes
Aperture is parameterized by f-stops or f-number
Credit, Wikipedia commons

## Slide 13: Cartesian Coordinate Systems

## Slide 14: Cartesian Coordinates for Images
Pinhole camera model
O
Image plane,
Optic Axis, z
Pinhole at origin
Object
Image
Principal Point

## Slide 15: Pinhole Camera
Pinhole camera is a canonical model for image formation
3-D real-world position translates to x-y position on image plane
Positions are defined relative to the optic axis,
Optical center, , is origin of coordinate system
x-y image plane position, , changes with optical center coordinates:
  - horizontal location with respect to optic axis
  - vertical location with respect to optic axis
  - distance from optic center along the optic axis
Pinhole camera image inverted

## Slide 16: Coordinate System for Pinhole Camera
Images are formed on an image plane
Place image plane between pin hole, origin, and object
  Image no longer inverted
  Simplifies transformations
Real-world and image plane coordinate along optic axis measured from optic center
Distance from origin to image plane is focal length,
  Simplify model by setting

## Slide 17: Pinhole Camera Model
Cartesian coordinates for a pinhole camera model
O
Image plane,
Optic Axis = z
Pinhole at origin
Principal Point

## Slide 18: Cartesian Coordinates for Images
Transform homogenous coordinates to cartesian coordinates
Transform from real-world to image plane coordinates
distance from origin to object
With inverse focal length , and w = distance from origin to image plane:
are all measured in real-world units, e.g. mm

## Slide 19: Focal Length
Short focal length
Long focal length
Field
of
view
Field
of
view
Changing focal length changes field of view a fixed distance
w
w
Image plane
Image plane

## Slide 20: Camera Models and Homogeneous Coordinates

## Slide 21: Homogenous Coordinates
Can form linear system of equations in homogenous coordinates
Define position on image plane and object:
Transform back to Cartesian image plane coordinates,

## Slide 22: Pinhole Camera Model
Homogenous coordinates for a pinhole camera model
O
Image plane,
Optic Axis
Pinhole at origin
Principal Point

## Slide 23: Transformations for Camera Model
Transform formations applied using pin hole camera model
Transformation between real-world and image coordinates require two sets of parameters
Intrinsic or camara parameters,
  – focal length
  – image array offset
  – skew correction, or idiosyncratic term
Extrinsic or camera pose, position and orientation parameters
  – Rotation matrix
  - translation

## Slide 24: Transformations for Camera Model
Extrinsic transformation for position and rotation comprises two independent operations
Rotation transformation,
Translation transformation,

## Slide 25: Pose Model in Cartesian Coordinates
Why use homogenous coordinates?
Consider an extrinsic transformation in cartesian coordinates:
or,
Where
  position vector on image plan
  position vector in world coordinates
  rotation matrix
  translation vector
An affine not a linear relationship!

## Slide 26: Homogenous Coordinates
Extrinsic transformation in homogeneous coordinates represented by a single matrix combining rotation and translation:
The complete extrinsic transformation in homogeneous coordinates:
A set of linear equations!

## Slide 27: Homogenous Coordinates
The complete extrinsic transformation in homogeneous coordinates:
Or,
This is a transformation from 3-d world coordinates to 2-d image plan coordinates
  is matrix
  is 3-d real-world object location in homogeneous coordinates
  is 2-d image plane location in homogeneous coordinates

## Slide 28: Pinhole Camera Model in Homogeneous Coordinates
We can project location of another plane onto an image plane in homogeneous coordinates for the pinhole camera model with common optical center
O
Image plane,
Optic Axis
Pinhole at origin
Principal Point
plane,

## Slide 29: Homogenous Coordinates
Transformation between points on planes in homogeneous coordinates represented by a single matrix combining rotation and translation:
The complete extrinsic transformation in homogeneous coordinates:
This is a transformation between 2-d locations on the plane

## Slide 30: Transformations for Camera Model
Intrisic transformation adjusts for characteristics of a camera
Intrinsic transformation comprised of three independent components
  Focal length,
  Image array offsets,
  Skew correction,
Intrinsic or Camera calibration matrix,
  And

## Slide 31: Transformations for Camera Model
How do we find the Intrinsic parameters of a camera?
Two ways to find intrinsic parameters
  Learn from multiple camera views of scene – more on this later
  Use multiple views of a known target
Wide variety of targets available commercially
Other suppliers

## Slide 32: Camera Model in Homogenous Coordinates
How can we construct the intrinsic transformation in homogenous coordinates?
  And
  A set of linear equations!

## Slide 33: Homogenous Coordinates
How to solve for the constant ?
In homogenous coordinates we can solve the three equations to find :

## Slide 34: Transformations for Camera Model
Complete homogeneous transformation accounts for camera pose and camera characteristics
Linear extrinsic and intrinsic transformations combined by matrix multiplication:
These equations are no longer linear
  depends on and vice versa!
  We will address this problem in subsequent lesson
Estimating the parameters requires solving a nonlinear optimization problem

## Slide 35: Four Transformation Problems

## Slide 36: Four Transform Problems
How can we simplify these planar transformations?
There are four levels of complexity
2-D Euclidean – Rotation and translation
2-D Similarity – Rotation, translation, and scaling
Affine - Rotation, translation, scaling, shearing
Projective – General transformation

## Slide 37: Four Transform Problems
How can we simplify these planar transformations?
We can construct the complete holmography as the product of simple transformations
2-D Euclidian – Rotation and translation
2-D Similarity – Rotation, translation, and scaling
Affine - Rotation, translation, scaling, shearing
Projective – Perspective point transformation

## Slide 38: Four Transform Problems
How can we simplify these planar transformations?
Model is restricted to planar transformations
Transformation matrices are constant over image
Assumes all objects in image are at a constant distance from image plane
How to overcome the limitations of the model?
  Can apply transformations over piecewise patches of the image, for example see implementation in Scikit Image
  Or, use a polynomial representation of parameters, for example see implementation in Scikit Image

## Slide 39: Four Transformations
2-D Euclidean transformation,
Planer operation
Applies rotation and translation
  a.k.a. rigid body transformation
3 degrees of freedom
  1 – rotation angle
  2 - translation
Simple cases
  Pure rotation – 1 DoF
  Pure translation – 2 DoF
Preserves shape, size , parallel lines

## Slide 40: Four Transform Problems
Planar 2-D Euclidean transformation – rotation and translation
Transformation from one 2-d plane to another can be defined in homogeneous coordinates
Multiply both sides by

## Slide 41: Four Transform Problems
Planar 2-D Euclidean transformation – rotation and translation
Can write the transformation in Cartesian coordinates
Or,

## Slide 42: Four Transformations
Planar 2-D Euclidean transformation
Pure rotation case:
1 DoF,
Right-handed coordinate system positive gives counter clockwise rotation

## Slide 43: Four Transformations
2-D Euclidean transformation
Pure translation case:
2 DoF,

## Slide 44: Four Transformations
Planar 2-D Euclidean transformation
Translation and rotation
3 DoF,

## Slide 45: Four Transformations
Planar 2-D similarity transformation
Planar operation
Applies rotation, translation and scale
5 degrees of freedom
  1 – rotation angle
  2 - translation
  2 – scale,
Preserves – angles, parallel lines

## Slide 46: Four Transform Problems
2-D similarity transformation – rotation, translation and scale
Transformation from one 2-d plane to another can be defined in homogeneous coordinates
The planar transformation is then:

## Slide 47: Four Transform Problems
2-D similarity transformation – rotation, translation and scale
Planar transformation from one 2-d plane to another can be defined in homogeneous coordinates
With , a scale factor,

## Slide 48: Four Transform Problems
2-D similarity transformation – rotation, translation and scale
Planar transformation from one 2-d plane distance D to another in homogeneous coordinates

## Slide 49: Four Transformations
Planar 2-D similarity transformation
Translation, rotation and scale
5 DoF,

## Slide 50: Four Transformations
Affine transformation
Planar operation
Applies rotation, translation, scale and shear
7 degrees of freedom
  1 – rotation angle
  2 - translation
  2 – scale
  2 – shear,
Preserves – parallel lines

## Slide 51: Four Transform Problems
Affine transformation – rotation, translation, scale and shear
Generalized planar affine transformation from one 2-d plane to another can be defined in homogeneous coordinates

## Slide 52: Four Transformations
2-D affine transformation
Translation, rotation, scale and shear
7 DoF,

## Slide 53: Four Transformations
2-D affine transformation
Translation, rotation, scale and shear
7 DoF,

## Slide 54: Four Transformations
2-D affine transformation
Translation, rotation, scale and shear
6 DoF,

## Slide 55: Perspective Transformations and Homography

## Slide 56: Projective Geometry
Projective transformation or homography
Perspective is determined by camera pose
Straight lines are not parallel in projective geometry
Straight lines meet at a vanishing point in a perspective view

## Slide 57: Projective Geometry
Projective transformation or homography
Perspective changes with camera pose
Vanishing point changes with perspective
Vanishing point is at infinity with orthogonal camera projection

## Slide 58: Changing Camera Pose
Camera pose determines the perspective on a scene
Start with a point in space X
X projected, with projective matrix P, at point x on image plane of camera 1 with optical center o
X projected, with projective matrix P’, at point x’ on image plane of camera 2 with optic center o’
We will fully explore this 3-D problem in a subsequent lesson

## Slide 59: Changing Camera Pose
Camera pose determines the perspective on a scene
Homography, , maps one perspective to another
Homography, , transforms between image planes with different camera centers

## Slide 60: Four Transformations
Planar Projective transformation or homography
Applies general transformation
aka the keystone transformation
Transformation effectively changes optical center or perspective point
8 degrees of freedom – scale independent
Preserves – straight lines, but nothing else

## Slide 61: Projective Transformation or Homography
General unrestricted transformation from one perspective plane to another can be defined in homogeneous coordinates
For planar transformation this becomes

## Slide 62: Projective Transformation or Homography
General planar unrestricted transformation from one perspective plane to another can be defined in homogeneous coordinates
Where is the perspective vector

## Slide 63: Projective Transformation or Homography
Example: Projective transform or homography
Effect of changing perspective vector
Only isotropic scale applied
Original image

## Slide 64: Projective Transformation or Homography
Example: Projective transform or homography
Effect of changing perspective vector
Only isotropic scale applied
Original image

## Slide 65: Summary
Planar transforms map between light scattered off objects and projections on a camera image plane
Planar projective transformation model based on pinhole camera
Planar transformations use projection matrix
  2-D Euclidean – Rotation and translation
  2-D Similarity – Rotation, translation, and scaling
  Affine - Rotation, translation, scaling, shearing
  Projective – General transformation, 8 DoF
Projective transform or homography maps one camera pose to another